# APU Panel

# Text boxes

## APU START/STOP Switch

Starts and stops the APU manually

If this switch is used to start the APU, it must also be used to shut it down

ON (Switch pressed and ON illuminated)

-Flashes when APU is starting. Steady when started and ready for use

-If APU shuts down due to fire, light flashes until the switch is selected to OFF

OFF (When pressed)

-Illuminates steady when APU shutdown is initiated

-APU bleed valve automatically closes

-APU shuts down 90 seconds after no longer supplying air

-Remains illuminated until shutdown is complete

APU GEN Switch

Pressed

-Resets APU Gen if Elec in manual mode

OFF (illuminated)

-Gen on speed, but malfunction has occurred

APU FUEL/FAIL/DOOR Status lights

FUEL (illuminated)

-Fuel pressure is too low

DOOR (illuminated)

-APU inlet door not fully open during start

-APU inlet door not fully closed after shutdown (The door begins to close appx 60 seconds after shutdown. Shutdown occurs appx 90 seconds after APU is no longer supplying air.  The door takes appx 12 seconds to close)

FAIL

-APU has failed, and start is not possible

ENG/APU FIRE TEST Button

When pressed:

-ENG and APU Fire Handles illuminate

-Fuel Switches illuminate

-Both Master Warning lights flash

-Fire Bell and aural warning tone sounds

-ENG 1,2,3 and APU FIRE alerts display

-ENG FIRE voice warning sounds

-(6) Eng FIRE AGT LOW lights and (2)

APU FIRE AGENT LOW (if installed)

illuminate

*When on battery power only, the Master

Warning lights, Fire Bell and FIRE alerts

will not activate

AGENT DISCH Fire Handle

Illuminates when an APU fire is detected, and automatically commands:

-Master Warning lights on

-EAD alert

-APU FIRE illuminates (red) on APU Fire Handle

-Fire Horn sounds near external APU Panel (nose gear area)

-APU shuts down

-Aural Warning sounds

-If equipped with 3rd, dedicated fire bottle, it will automatically discharge

Pulling the APU Fire Handle:

-Emergency APU shutdown

-Fire extinguishing agent is armed to discharge

-APU Generator disconnects / de-energized

-APU Fuel Valve closes

-#2 Engine bleed valve closes

Rotating the handle (after pulling):

-(Clockwise) Discharges fire bottle #1 (shared with engine 2)

-(Counterclockwise) Discharges fire bottle #2 (shared with engine 2)

APU Auto Shutdown:

-Overspeed or loss of N1or N2 signal   -High EGT or loss of EGT signal

-Low oil pressure or high oil temp        -No light-off during start, or slow start

-Reverse flow in bleed air system         -Inlet door not open, or power failure

-Fire warning	              	         -Loss of DC power

APU Fire Agent Bottle Configuration

The APU and Engine 2 both share the same two fire agent bottles for fire protection. In addition, some MD-11s are also equipped with a third fire bottle that is dedicated only to APU fire protection. If not equipped with the third (dedicated) APU fire agent bottle, discharging both fire agent bottles into engine 2 will leave no fire agent remaining for APU fire protection.

In order to discharge the fire agent bottles that are shared with engine 2, the APU fire handle on the APU Panel must be manually pulled and rotated.

If the third, dedicated fire bottle is installed, it will automatically discharge if an APU fire is detected. If this dedicated fire agent bottle is discharged, the fire agent bottles that are shared with engine 2 are still available for additional APU fire fighting, or for engine 2 fire protection.

APU In-Flight Parameters

Start      Up to 25,000 ft.

Run       Up to 30,000 ft (electrical only)

APU FIRE AGENT (1,2)

Low Light

Associated with APU fire bottles 1 & 2 that are shared with engine 2. These lights are not installed on all MD-11s

### LOW (illuminated)

Associated fire bottle has been manually discharged

APU FIRE AGENT 3 DISC/LOW Switch

### This switch is only installed on aircraft that have the third, dedicated APU fire bottle installed.

### LOW (illuminated)

### Respective fire bottle has been automatically or manually discharged

DISC (illuminated)

APU Fire Handle

has been pulled

### DISC Switch Pressed

Manually discharges fire

bottle 3 (if auto discharge

fails – APU fire handle

must be pulled before

switch is pressed)