CVR / Bus Fault / Cargo Temp Controls

# Text boxes

COCKPIT VOICE RECORDER

TEST / ERASE Buttons

TEST (Pressed)

Minimum of level 8 during test

ERASE (Pressed)

Can only be accomplished on ground with parking brake set

## GEN BUS FAULT RESET

### Maintenance use only

### Not to be used by Flight Crew

BUS _ FAULT (illuminated)

-Switch is used to reset the associated Generator Control Unit

FWD CARGO TEMP Control

Controls temperature in lower FWD cargo compartment by regulating system 3 pneumatic flow to jet pumps.

LO to HI

Selection options are either 40 o or 70 o

# OFF

Heating system is off

AFT CARGO TEMP Control

Controls temperature in lower AFT cargo compartment by regulating system 2 pneumatic flow to jet pumps.

Cold to hot

Selection range is from 39.5 o to 95.5 o

# OFF

Heating system is off