FMA Annunciations

# Text boxes

# SPEED

# Annunciation	               Speed Control Mode         Color		Type

IDLE THRUST	               FMS descent	    Magenta                 Engaged

###### PITCH		               Speed on pitch                  Magenta/White     Engaged

THRUST		               Speed on thrust                Magenta/White      Engaged

RETARD		               Throttle retard                 White  	                  Engaged

###### WINDSHEAR	               Windshear FPA control  White	                  Engaged

LO SPEED PROTECTION    Low speed protection      White        Armed/Engaged

HI SPEED PROTECTION     High speed protection     White        Armed/Engaged

# ROLL

# Annunciation	Roll Control Mode                Color	Type

VOR1 or VOR2	Capture/Track VOR	    White	 Engaged

LOC ONLY	Capture/Track LOC	    White	 Engaged

NAV1 or NAV2	FMS Nav	    Magenta	 Engaged

HEADING ______	Heading Hold or Select   White	 Engaged

TRACK _____	Track Hold or Select	    White	 Engaged

ROLLOUT	Landing Rollout	   Green/White	 Engaged

LOC	Localizer	   Green/White	 Engaged

ALIGN	Runway Alignment	   Green/White	 Engaged

TAKEOFF	Takeoff Ground Roll	   White	 Engaged

VOR 1 (or2) CRS	Over VOR	   White	 Engaged

NAV ARMED	FMS Nav Armed	   Magenta	 Armed

LAND ARMED	Land Armed	   White	 Armed

LOC ARMED	LOC Armed	   White	 Armed

VOR ARMED	VOR Armed	   White	 Armed

# ALTITUDE

# Annunciation	 Altitude Control Mode                Color	           Type

T/O THRUST	Takeoff Thrust	White/Magenta	Engaged

T/O CLAMP	Throttles Clamp	White/Magenta	Engaged

CLB THRUST	Climb w/Climb Thrust	White/Magenta	Engaged

HOLD	Altitude Hold	White/Magenta	Engaged

MCT THRUST	Climb w/Max Cont. Thrust	White/Magenta	Engaged

V/S	Vertical Speed	White/Magenta	Engaged

FPA	Flight Path Angle	White	Engaged

### PROF	FMS Profile Descent	Magenta	Engaged

GO AROUND	GA Thrust Mode	White	Engaged

G/S	Glideslope	White/Green	Engaged

DUAL LAND	Dual Land	Green	Engaged

SINGLE LAND	Single Land	White	Engaged

APPR ONLY	No Land Mode	White	Engaged

FLARE	IIIA/B Autoland Flare	White/Green	Engaged

ROLLOUT	IIIA/B Autoland Rollout	White/Green	Engaged

IDLE CLAMP	Level Change Descent	White	Engaged

IDLE	FMS Speed on Elevators	Magenta	Engaged

PROF TO	Next FMS Prof Altitude	Magenta	Armed

PROF ARMED	PROF Armed on Ground	Magenta	Armed

###### VERT ALERT	Altitude change in PROF Mode   Magenta	Armed

LAND ARMED	Armed to Capture G/S	White	Armed

###### WINDSHEAR	Windshear (G/A Thrust) Mode   White	Engaged

G.A THRUST	Climb w/GA Thrust	White/Magenta	Engaged

CLB THRUST	Climb w/Cruise Thrust	White/Magenta	Engaged

## Annunciation Colors

White       =    Manual

### Magenta   =    FMS

#### Green       =    Autoland

Engaged modes display as large font on lower line.  Armed modes display as small font above Engaged mode

##### Flight Mode Annunciator