MD-11 FMS Initialization

AC STATUS – Displays when powered up, or press REF , then press AC STATUS prompt.

To change active database, select new DB. Press CONFIRM prompt to activate.

Complete Flight Plan Uplink

Select F-PLN INIT prompt on AC STATUS page, or press the INIT key.  Complete the F-PLN, Weight and Fuel pages.

F-PLN Page

--If FPLN uplink unavailable, Enter KORG/KDST

--Enter KALT (O’s if none)

--Adjust present position with slew keys (if GNS POS not displayed)

--Select “Initialize IRUs”

--Enter Flt Number (min 4 characters)

--Enter Cruise FL’s (separate with /’s)

--Enter cost index

Weight (press       )

--Enter taxi and block fuel

--(TOGW & ZFWCG filled in later)

Fuel (press       )

--Enter refuel quantity

--Enter ballast (if req’d)

--If ballast req’d, enter 2, U or T

Modify Uplinked Route, or build route

Press F-PLN key

--Select KORG (goes to lateral rev page)

--Select Runway (<SEL>)

--Select SID (<SEL> will be displayed)

--Select Transition (<SEL>)

--Select *INSERT

Waypoint Entry (Via airway, direct entry, place/brg/dst, place/dst, lat/long)

Airway

--Select wpt that is start of airway

--Select AIRWAYS

--Enter airway ID in scratchpad & move to VIA prompt

--Enter ending waypoint in scratchpad & move to TO prompt

(or if airway to intercept another airway, enter 2nd airway in 2nd VIA)

--After airways have been entered, select *INSERT prompt

Direct Entry

--Enter waypoint in scratchpad & move to point on plan where waypoint is to be inserted. Moving to point on plan inserts waypoint and moves subsequent waypoints down.

STAR

--Select waypoint that is beginning point of STAR

--Select STAR prompt

Discontinuities

--Clear (if desired) by pressing CLR key, then select FLIGHT PLAN DISCONTINUITY line.  This creates a direct route between two points that previously were not connected.

Verification of Entries

Progress Page - Go to progress page & verify total distance against flight plan distance

EFIS

--Select PLAN on ECP (EFIS Ctrl Panel)

--Select F-PLN on FMC; use slew keys to step through route

(ND will show a “North-up” view of route)

--Reselect MAP on ECP

Complete Wind Data Uplink

Changes to Route

New SID or STAR requires deletion of old STAR, and reselection of new STAR, even if it is the same STAR, but with different transition.

(Select ORG, select STAR, press CLR, select old STAR,

select STAR, select transition, select runway – new STAR

is now entered)

Add or delete waypoints as necessary for compliance with clearance.

Copy flight plan to Secondary – Select SEC F-PLN key. Select COPY ACTIVE prompt.  Route changes are made to secondary plan, then activated.

Load ZFW, ZFWCG and TOCG from load manifest in Weight page of INIT .

Complete TO/APPR page

-- Enter FLEX value (assumed temp) from OPS (if desired)

--Select appropriate THRUST LIMIT if FLEX is used

--If max thrust T/O is desired after already selecting FLEX,

press CLR, and select FLEX (deleted flex)

--PACKS field toggles packs on/off

--Enter T/O flaps from OPS

--Enter slope & wind (use +/-, U/D, H/T)

--Enter OAT (ex. 85F, or 33C)

--Confirm v-speeds (or modify). Selecting values with an

“ * ” will activate and display them on PFD speed tape

Clearing v-speed will redisplay FMS calculated v-speed

--Enter level-off in engine out acceleration field

Note: A difference of greater than 2% between the load manifest TOCG and the calculated CG on the Secondary Engine Page should be resolved before departure.