# MD-11 F/O Cockpit Prep

Entry Doors	Check

Chk pneumatic bottle press. and slide inflation low pressure light/gauge

Logbook	Check

Circuit Breakers	Check

Weather Radar	Off

Fuel Switches	Off

Parking Brake	As Rqd

Spoiler & Flap/Slat Handles	Check

Gear Handle	Down

Fuel Dump/Manifold Drain Switches	Check

Emergency Power Selector	Off

Battery Switch     Batt bus off light extinguishes	On

External Power	On

AC/DC 1/2/3 Off lights and all Bus Off lights extinguish,

Ext Pwr On and Gen 1/2/3 Arm lts Illuminate

Engine/APU Fire Test-AC Busses Powered, or	Check

Eng and APU fire handles, Mstr Wrng Light, and all fuel

Switches illuminate. Fire bell, attn tone and “Eng 1(2-3) Fire”

voice annunciations sound. “ENG 1 (2-3) FIRE” and “APU FIRE”

EAD alerts display. On some acft, Eng and APU Fire AGT low

lights illuminate. With button pressed, push Mstr Wrng to silence.

Engine/APU Fire Test-Battery Power Only	Check

All Eng and APU fire handles, Mstr Wrng Light, and all fuel

switches illuminate. On some acft, Eng and APU Fire AGT low

lights illuminate.

APU Power	As Rqd

IRS Cargo Fire Test	Check

Cargo Fire Test on EAD and Heat/Smoke/Disag/Low/

Mstr Wrng/Test lights all illuminate  (4 Red, 4 low, 2 DISAG)

ACARS INIT “REQ” prompt    (Initiates FPL uplink)	Press

Emergency Equipment/Fire Ax	Check

Fire Extinguishers	Check

PBE	Check

PSELT	Check

Escape Ropes	Check

Life Vests	Check

First Aid Kit	Check

Oxygen Bottle	Check

Manuals	Check

Rear Cockpit Area	Check

Supernumerary Area	Check

Supernumerary Oxygen	Check

Bulkhead Door	Check

Smoke Curtain	Check

Annunciator Lights	Check

Verify Trim Air Off light extinguished before pressing, aural

overspeed and Air Sys Test annunciated on EAD. X’s and

8’s displayed and all lights (no Mtx int. and Mic lts)

Air Conditioning   	On

Verify cabin press in auto and O/F valve open

IRS Initialization 	Check

Accept uplinked Secondary Flight Plan, then activate Secondary Flight Plan. If

flt plan uplink unavailable, load ORG/DST/ALT, verify PPOS, then initialize.

Quick align on through flights (IRS Off/On within 5 seconds)

Voice Recorder	Check

Gen. Bus Fault Reset Panel	Check

Cargo Temperature	Set

FADEC Mode Panel	Check

Engine Ignition	Off

Hydraulic Control Panel	Check

Clear with Mtx, press test button, Hyd Press Test annunciated

(Confirm flt controls are clear)

Electrical Control Panel	Check

Verify “Batt Charging” not displayed – Emg Pwr selector to ARM

Emg Off light extinguishes, EMG pwr on illuminates for 30 secs

Air Control Panel	Check

Fuel Control Panel (chk total fuel qty and fuel slip)	Check

Emergency Light Switch	Check

Arm, and press to test – Emg Lts Test Pass illuminates

No Smoking/Seat Belt Switches	On

Exterior Lights   (Nav lts on)	Set

GPWS	Check

(After IRS Init) Verify Terrain Ovrd switch not in OVRD.

Press WXR and verify TERRAIN displayed in lower right

corner of ND. Move GPWS switch to test. Verify aural and

visual annunciations operative. G/S inhibit light illuminates

and test pattern on ND. Grnd Prox on PFD during test.

Auto Flight System Control Panel	Check

Cabin Pressurization 	Check

Auto, O/F valve open, Ditching switch guarded

Anti-Ice/Windshield Control Panel	Set

Defog on

Fuel Used Reset Button	Reset

Flight Instruments 	Set

IAS, Desired Hdg, Altitude, RA, Bank Angle auto,

AFS Ovrd switches up, QNH, Trfc-Data, VOR, No “Xs”

Oxygen System and Mask	Check

Source Input Select Panel	Check

Static Air Selectors	Norm

Display Units	Check

Clock	Check

Gear Warning System	Check

Select CONFIG, verify green, pull handle, config turns red

and red wrng lts illuminate

Standby Altimeter/Airspeed/Attitude (Set)	Check

Anti-Skid (Off, light extinguished)	Check

Autobrakes	Off

Slat Stow Switch (light extinguished)	Check

Takeoff Warning System 	Check

Throttle lever 1 fwd/back, Throttle 2/3 fwd/back – horn on both

System Display Status Page	Check

Communication Radio Panel 2	Set

Audio Control Panel 2	Set

Weather Radar (Test pattern, test sys 1 and 2)	Check

Transponder/TCAS (After IRS Init - Press to test)	Check

Communication Radio Panel 3	Set

Trim (Rudder/Aileron zero)	Check

ADG Release Handle	Check

FMS (Flt Pln, Wind uplink, T/O Appr (OAT), Nav/Rad	Load

Cockpit Window	Check

OPS Computer	On

## MD-11 Capt Cockpit Prep

Logbook	Check

Flight Instruments	Set

Oxygen System and Mask	Check

Source Input Select Panel 	Check

Capt EIS to AUX, then back to 1

Static Air Selectors	Norm

Display Units	Check

Clock	Check

IRS Present Position	Check

Communication Panels	Check

Audio Control Panels	Set

FMS   (IRS Pos, PROG-DTG, INIT pages, FPL) 	Check

ACARS	     (Complete) Initialization

Cockpit Window	Check

### Before Start Checklist

Note – Boxed items not required on quick turn-around